## Slide 1: Team 05: Calvin Bolt 3.0

## Slide 2: Team Members
Nathan Swaim
ME
Bernice Portugal
ME
Samuel Hanover
ME
Phillip Kim
ME

## Slide 3: Presentation Outline
Project Overview
Accomplishments
  Version Control Software
  Braking System
  Steering System
Design Norms
Ideas for Future Groups

## Slide 4: Project Overview: Calvin Bolt 3.0
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
Overall Focus:
Create a platform of continuous improvement for future students in hopes of providing a visual representation of Calvin Engineering.
Improving certain systems rather than entire vehicle
  Braking System
  Steering System
Improve documentation through version control software

## Slide 5: Version Control Software
Project Overview
Braking System
Steering System
Future Groups
Design Norms
Version Control Software
http://www.autodesk.com/products/vault-family/overview
Tracks CAD Revisions
Adaptable to any CAD software
Store Microsoft Office Documents (i.e. Excel, Word)

## Slide 6: Braking System
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
The Goal:
Be able to provide a pulling force greater than 300 lbf. when applying 45 lbf. to the pedal.
µ = 0.3
µ = 0.7

## Slide 7: Braking System
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
The Original Plan:
Use a master cylinder with a smaller diameter and a higher pivot point. The closer the distances of “D” and “d” are, the higher the provided force by the master cylinder is.
D
d
Fixed
Flexible
d
Shaft
Pedal
Pivot Point
Shaft

## Slide 8: Braking System
Issues:
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
Issues | Solution | Did it work?
Piston Rod Broke | Create new rod | Improved, but no
Fluid Leakage from Caliper | Purchased new caliper | Improved, but no
Losing Pressure | Pressure Check | No, pressure was working fine

## Slide 9: Braking System
The Revised Plan:
Use the 5/8” master cylinder with a higher pivot point and an increase in leverage from the geometry of the pedal to make up for the loss force in having a larger master cylinder.
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 10: Braking System
The Final Plan:
Increase the length of the brake pedal by 3”
This number was calculated from our theoretical model.
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 11: Braking System
The Results:
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 12: Steering System
Ackermann Steering
Bump Steering
Steering degree Ratio
Shaft Supports
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 13: Ackermann Steering
www.slideshare.net
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 14: Bump Steering
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms

## Slide 15: Steering Degree Ratio
Standard Ratio: 12:1 to 20:1
Previous Ratio: 11:1
Current Ratio: 25:1
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
Project Overview

## Slide 16: Shaft Supports
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
Project Overview

## Slide 17: Design Norms
Trust
Stewardship
Integrity
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
www.linkedin.com

## Slide 18: Idea for Future Groups
Project Overview
Version Control Software
Braking System
Steering System
Future Groups
Design Norms
Implementing ABS
Aesthetic Appeal
Frame
Higher Efficient Batteries
Higher Seating Capacity
Lighting
And more…

## Slide 19: Questions?